## Slide 1: HEXAPOD - a six legged Robot
-Nisarg K. Patel [EC099] id=22ecuos113
-Krish S. Patel [EC097] id=22ecuos026

## Slide 2: CONTENTS
Project Overview
Key Components & Specifications
Hardware Architecture
Power Management System
Control System
Motion Control & Inverse Kinematics
Vision System
Costing
Challenges & Solutions
Future Improvements

## Slide 3: What is a Hexapod
As it's name suggests, it is a six legged robotic platform designed to mimic the locomotion of insects.
This design offers a exceptional stability and is adaptable to most of the terrains such as uneven terrains i.e forests, rocky surfaces , soft terrains i.e deserts and mud etc.
This is possible because it is a synchronous 3 leg movement. When 3 legs are moved up for going forward other 3 legs gives a full stability which make this robot different from other.

## Slide 4: OVERVIEW
The Hexapod is an advanced six-legged robot platform designed for stable locomotion across various terrains. Inspired by insects, the hexapod design offers exceptional stability and adaptability compared to wheeled or bipedal robots.
Our implementation features:
18 degrees of freedom (3 servos per leg)
Real-time video streaming capabilities
Custom battery management system
Programmable walking gaits
Obstacle avoidance

## Slide 5
KEY COMPONENTS
AND
SPECIFICATIONS

## Slide 6: Major Components
MG996R Servo motor
Arduino Mega
BLUETOOTH Module –HC-05
ESP32 CAM MODULE
BUCK CONVERTERS
3S 100A LIFEPO4 BMS

## Slide 7: BLOCK DIAGRAM

## Slide 8: ARDUINO MEGA
SPECIFICATIONS:
Microcontroller: ATmega2560
Operating Voltage: 5V
Input Voltage: 7-12V (recommended)
Digital I/O Pins: 54 (15 with PWM)
Analog Input Pins: 16
Flash Memory: 256 KB
Clock Speed: 16 MHz

## Slide 9: MG996R SPECIFICATIONS
Operating Voltage: 4.8V to 6V DC
Operating Speed: 0.19 sec/60° at 4.8V, 0.14 sec/60° at 6V
Stall Torque: 9.4 kg·cm (4.8V), 11 kg·cm (6.0V)
Dead Band Width: ≤ 5 µs
Working Angle: 0° to 180°
Maximum Rotation Angle: 0° to 360° (if modified)
Weight: 55g
Dimensions: 40.7 x 19.7 x 42.9 mm
Gear Type: Metal gears
Motor Type: Coreless motor
Connector: 3-pin (Orange: Signal, Red: VCC, Brown: GND)
Current Draw: Idle: 10 mA, Operating: 170-180 mA, Stall: ~2.5 A
Applications: Robotics, RC vehicles, hexapods, control arms.

## Slide 10: BLUETOOTH MODUEL HC05
Protocol: Bluetooth 2.0+EDR
Frequency: 2.4GHz ISM band
Modulation: GFSK (Gaussian Frequency Shift Keying)
Communication Range: ~10 meters
COMMUNICATION : UART
Default Baud Rate: 9600 bps (configurable 1200-115200)
Operating Voltage: 3.3V-6V (5V typical)
Current: 30mA (typical)
Working Mode: Master/Slave switchable
Default Password: "1234" or "0000"

## Slide 11: ESP32 CAMERA MODULE
ESP32-S Dual Core processor
OV2640 2MP camera
Wi-Fi connectivity for streaming
Real-time video transmission
Resolution: Up to 1600×1200
Frame Rate: Up to 25 fps
Primarily, uses Wi-Fi (IEEE 802.11 b/g/n) and Bluetooth (4.2 BR/EDR and BLE) protocols.

## Slide 12: BMS MODULE
3S LiPo Battery Configuration (11.1V)
100A Battery Management System (BMS)
Features:
Cell balancing
Overcharge/discharge protection
Short circuit protection

## Slide 13: BUCK CONVERTER
Type: DC-DC Buck Converter (Step-Down)
Power Capacity: 300W
Output Current: 20A (Max)
Applications: LED driver, battery charging, vehicle power supply, and more.
Input Voltage:
Range: 6V to 40V DC
Output Voltage:
Range: Adjustable from 1.25V to 36V DC
Other Key Specifications:
Efficiency: Typically around 97%
Switching Frequency: Around 180 kHz
Output Ripple: ≤ 50mV

## Slide 14: BATTERY PACK - 12000mAH
CONNECTED IN 3 SERIES CONNECTION.
EACH 3000mAH CELL connected parallely with other 3 cells, I,e 4 cells in parallel.
And those 4 cell box each connected in series with other two 4 parallel cell boxes.

## Slide 15: Circuit diagram

## Slide 16: Costing
COMPONENT | PRICE
Servo motor (x18) | 6300
ARDUINO MEGA | 1300
3S 100A BMS | 450
BUCK CONVERTERS (4 PIECES) | 900
ESP32 CAMERA MODULE | 550
Bluetooth module | 250
3-D printed body parts | 5600
BATTERY CELLS ( 12 PIECES) | 1080
BATTERY HOLDERS, WIRES | 220

## Slide 17
COMPONENT | PRICE
PAN AND TILT COUPLERS | 530
BATTERY INDICATOR | 45
JST-SM CONNECTORS | 20
DC PIN PLUGS | 45
TOTAL | 17290/- RS

## Slide 18: Setup-module working

## Slide 19: Challenges and solutions:
1. Locomotion and Gait Complexity
Challenge
Designing stable and efficient walking patterns for six legs is significantly more complex than bipedal or quadrupedal robots.
Solutions
Implement adaptive gait algorithms that can dynamically adjust leg movements
Use inverse kinematics to calculate precise leg positioning
Develop terrain-aware walking algorithms that can:
  Detect surface irregularities
  Adjust leg placement in real-time
  Maintain center of gravity during movement
2. Mechanical Stability
Challenge
Ensuring structural integrity while maintaining lightweight design and flexibility.
Solutions
Use advanced materials like carbon fiber or aerospace-grade aluminum
Design modular leg mechanisms with:
  High-precision servo motors
  Robust joint connections
  Shock-absorbing mechanisms
Implement sophisticated balance control systems using:
  Gyroscopic sensors
  Accelerometers
  Distributed weight sensing

## Slide 20
3. Power Management
Challenge
Managing energy consumption across six independent leg actuators and control systems.
Solutions
Develop efficient power distribution architecture
Use brushless DC motors with high efficiency
Implement adaptive power management:
  Dynamic voltage scaling
  Intelligent sleep modes for inactive leg systems
  Energy recuperation during movement
Control System Complexity
Challenge
Synchronizing six independent legs with precise coordination and minimal computational overhead.
Solutions
Distributed computing architecture
Use of FPGA or dedicated microcontrollers for leg control
Implement hierarchical control systems:
  Low-level PID controllers for individual leg movement
  High-level path and gait planning algorithms
  Machine learning adaptive control mechanisms

## Slide 21
Thank you